## Slide 1: Probabilistic Safety Verification of Autonomous Systems: A Statistical Approach for Monitoring
Bineet Ghosh1 Étienne André2 FORTE 2025
1Bineet Ghosh is with the Department of Computer Science, The University of Alabama, USA.
bineet@ua.edu
2Étienne André is with the Université Sorbonne Paris Nord, LIPN, CNRS UMR 7030, Villetaneuse, France and a member of Institut universitaire de France. etienne.andre@lipn.univ-paris13.fr

## Slide 2: In the Event of a Crash!
Cause of the crash?
Who was at fault?

## Slide 3: Investigating the Crash
Stores information of the vehicle/plane until the time of crash.
Flight Black Box
Detecting safety violation from the stored information.
Notes: * Typically stores: states of the system, the control inputs, sensor data etc.

## Slide 4: The Stored Information (Logs)
Logs
=0
Stores the information of the current state of the car
Notes: * Consider this toy example of a vehicle that is about to experience an engine breakdown

## Slide 5: The Stored Information (Logs)
Logs
Stores the information of the current state of the car
=0
Acceleration with an error range.
Distance to the lead vehicle.
Velocity with an error range.
Stored Information
Notes: * Real world sensors are not perfect - they typically have errors associated with them

## Slide 6: The Stored Information (Logs)
Logs
=0
Acceleration with an error range.
Distance to the lead vehicle.
Velocity with an error range.
Note: the gathered logs can have added noise—due to sensor errors.
The gathered logs are an over-approximation of the actual states.
Notes: So it certainly contains the actual state – with some extra added noise around it

## Slide 7: The Stored Information (Logs)
=0
=1

## Slide 8: The Stored Information (Logs)
=0
=1
Not Logged at !
Notes: * This could be due to energy saving policies, sensor failure, etc.

## Slide 9: The Stored Information (Logs)
=0
=1
=3

## Slide 10: The Stored Information (Logs)
=0
=1
=3
Not Logged at !

## Slide 11: The Stored Information (Logs)
=0
=1
=3
=5
Engine breakdown!

## Slide 12: The Stored Information (Logs)
=0
=1
=3
=5
Engine breakdown!
What caused the engine breakdown?
Need to answer this question from the (noisy) logs.
Was an unsafe maneuver made by the vehicle at time steps with no logs?
=2
=4

## Slide 13: Monitoring: Logs
Logging at every time step.
Logging at some time steps.
Unsafe region!
Did the system reach the unsafe region at missing log steps?
Main Idea: Reconstruct the missing logs!
Notes: * Consider this example of logging, where x axis is time, and y axis is the value of a state variable x. The dark blue dots are the gathered logs, and the light blue dots are missing logs.

## Slide 14: Monitoring: Naïve Approaches
Green dots represent reconstructed samples.
Blue dots represent the scattered logs.
Three possible reconstruction of the missing logs.

## Slide 15: Monitoring: Naïve Approaches
Green dots represent reconstructed samples.
Blue dots represent the scattered logs.
Reconstructed using piecewise-constant or linear approximation.
Problems:
Often models the behavior inaccurately!
Can yield a “safe” answer, while the actual system might have been unsafe (unsound).

## Slide 16: Monitoring: Naïve Approaches
Reconstructed assuming arbitrary dynamics.
Problems:
Always yields potentially “unsafe”!
Removes interest of monitoring!
Green dots represent reconstructed samples.
Blue dots represent the scattered logs.

## Slide 17: Monitoring: Logs
Logging at every time step.
Scattered Logging.
Scattered & Noisy Logging.
Considered in this work.
Notes: Note: in both these examples, the gathered logs are exact. I.e., at every time step, the exact values of the state variable is gathered.
But it in reality, this can seldom be the case, as the sensors used for gathering data are noisy. So as a result, what we have is a range of values instead of an exact value.

## Slide 18: Monitoring: Main Challenge
Logging at some time steps.
Unsafe region
Main Idea: Reconstruct the missing logs!
Operation
“Formal” Model of the System’s Behavior?
Complex – thus making formal techniques unscalable.
Unavailable – for complex components such DNNs and Simulink models.
Notes: Once the AS is in operation, it will gather some scattered and noisy logs
Now recall, the main idea is to reconstruct the missing logs. That is the behaviors, between the blue bars here.
Now to reconstruct the behavior between to blue bars, one needs to consider all possible behaviors, that typically represented as reachable sets. Represnted by the blue pipes
Now to compute such reachable sets, one needs to have a formal model of the system behavior.
For real world systems, these formal models are extremely complex……

## Slide 19: Monitoring: Main Challenge
Logging at some time steps.
Unsafe region
Main Idea: Reconstruct the missing logs!
Operation
I/O Execution Model
Digital replica of the actual system.
Generates random trajectories/behaviors from an initial state
In this Work!
No Formal Model Needed!
Notes: In contrast, in this work, we consider…..

## Slide 20: Monitoring: Main Idea
Operation
I/O Execution Model
Log
Unsafe region
Step 1: Create random trajectories from the log
Using
These trajectories recreate potential behaviors of the system from the log
Notes: Let us go through the main idea of the monitoring approach proposed in our work
It is worth noting, that between every possible logs, we are generating random trajectories, and not pipes of reachable unlike what we saw in our last slide.

## Slide 21: Monitoring: Main Idea
Operation
I/O Execution Model
Log
Unsafe region
Step 2: Check safety
System Safe: If all the random trajectories are safe
System Unsafe: If an unsafe trajectory is found
Concrete counterexample/behavior violating safety property

## Slide 22: Monitoring: Main Idea
Operation
I/O Execution Model
Log
Unsafe region
But!
How many such random trajectories do we need to check?
Clearly, there are infinitely many such trajectories
Ans: Only trajectories!
Still Sound?
Yes, with high probabilistic guarantees!
Safe for practical purposes, suitable for complex systems
computed using statistical hypothesis testing
Notes: * As we saw, we simply generating trajectories between the logs, and not pipes. That is, these trajectories represent only one possible behavior, and not all possible behaviors.

## Slide 23: Monitoring: Main Idea
Operation
I/O Execution Model
Log
Unsafe region
Driving Philosophy!
Make Autonomous Systems Trustworthy!
Safe for practical purposes with a high level of confidence
Trades of Formal Guarantees, with Statistical Guarantees.

## Slide 24: Monitoring: Main Idea
Operation
I/O Execution Model
Log
Unsafe region
Driving Philosophy!
Make Autonomous Systems Trustworthy!
Safe for practical purposes with a high level of confidence
Trades of Formal Guarantees, with Statistical Guarantees.
Unscalable or unavailable for complex systems with DNN, Simulink or black box based components

## Slide 25: Monitoring: Main Idea
Operation
I/O Execution Model
Log
Unsafe region
Driving Philosophy!
Make Autonomous Systems Trustworthy!
Safe for practical purposes with a high level of confidence
Trades of Formal Guarantees, with Statistical Guarantees.
Efficient for complex systems, and provides high confidence safety guarantees for practical purposes

## Slide 26: Monitoring: Overview
Step 0: Computing (Statistical Hypothesis Testing)
Formulate hypothesis
Hypothesis Selection
Analyze random sample trajectories to select between and
Note: denotes the system is safe
Compute
Such that if all random trajectories are safe, is selected
Such a closed form can be obtained based on
Notes: * Now let us go through the overview of the approach.

## Slide 27: Monitoring: Overview
Step 1: Create random trajectories from the log
I/O Execution Model
Log
Unsafe region
Valid Trajectory?
Not intersecting all logs
Such a behavior was never witnessed during its execution

## Slide 28: Monitoring: Overview
Step 1: Create random trajectories from the log
I/O Execution Model
Log
Unsafe region
Valid Trajectory?
Intersecting all logs
Such a behavior was witnessed during its execution

## Slide 29: Monitoring: Overview
Step 1: Create random trajectories from the log
I/O Execution Model
Log
Unsafe region
Generate valid random trajectories?
Step 1.1. Generate a random trajectory with the first log-sample as initial set
Step 1.2 (Check Validity). If invalid: reject and repeat (until valid random trajectories are obtained)

## Slide 30: Monitoring: Overview
Step 1: Create random trajectories from the log
I/O Execution Model
Log
Unsafe region
Generate valid random trajectories?
Step 1.1. Generate a random trajectory with the first log-sample as initial set
Step 1.2 (Check Validity). If valid: proceed to next step

## Slide 31: Monitoring: Overview
Step 2: Check safety
I/O Execution Model
Log
Unsafe region
If unsafe. Return as a concrete counterexample
Process ends. System unsafe, with concrete counterexample.

## Slide 32: Monitoring: Overview
I/O Execution Model
Log
Unsafe region
Step 2: Check safety
If safe. Proceed to next step.

## Slide 33: Monitoring: Overview
I/O Execution Model
Log
Unsafe region
Step 3: How many trajectories checked?
If less than trajectories checked. Proceed to a new valid trajectory generation

## Slide 34: Monitoring: Overview
I/O Execution Model
Log
Unsafe region
Step 3: How many trajectories checked?
If trajectories checked. Terminate the process
System is inferred as statistically safe with probability

## Slide 35: Case Study: Jet Model
To evaluate our approach under realistic jet engine dynamics in no-stall mode.
Dynamics
State Variables
Mass flow
Constant
Pressure rise
Jet engine dynamics based on the Moore-Greitzer model
Operates in no-stall mode with stabilizing feedback control

## Slide 36: Case Study: Jet Model
To evaluate a safety monitoring approach under realistic jet engine dynamics in no-stall mode.
Dynamics
State Variables
Safety. Mass flow of the jet model is maintained at:
Imagine a crash scenario where the only available data for analysis is the log recorded by the jet prior to the crash
Operation
Safe?

## Slide 37: Jet Model: Random Behaviors

## Slide 38: Jet Model: Monitoring Tasks
Given: Log of the jet
Task 1: Impact of logging frequency (number of records in the log) on safety inference.
Task 2: Impact of uncertainty (in log records) on safety inference.
Number of records
Amount of uncertainty

## Slide 39: Jet Model: Results
Logging frequency
Uncertainty
Black: Log records
Red dotted: Safety constraint
Colored Lines: Random trajectories
Safe!
Safe!
Unsafe!
Increasing Uncertainty. Increased chances of finding a counterexample.
Increasing Logging Frequency. No significant impact.
Unsafe!

## Slide 40: Conclusion
Trades-off formal safety guarantees with high-confidence probabilistic assurances
Trustworthy monitoring suitable for most practical applications
SHT-based framework to detect safety violations from a log with noisy and missing records
Successfully monitored non-linear and DNN benchmarks in under 250 seconds

## Slide 41: Artifact Evaluated Tool: Posto
github.com/bineet-coderep/posto
Scan this QR code on your phone
Thank You!