## Slide 1: Trustworthy Autonomy Lecture 3
Bineet Ghosh
bineet@ua.edu

## Slide 2: Uncertainties with an Example: Anesthesia
Initial concentration level of ()
Initial concentration level of ()
Initial concentration level of
Initial concentration level of
Injected drug
https://cps-vo.org/node/12111
Notes: As an illustration, let us consider the following initial concentration levels.

## Slide 3: Uncertainties with an Example: Anesthesia
After time
Using the dynamics, compute the concentration levels after time
Initial Set
Reachable Set at time

## Slide 4: Uncertainties with an Example: Anesthesia
Reachable sets are a tool for safety verification
Check if concentration levels are safe
Notes: Now the question is, why do we care about computing reachable sets?
  We care about computing reachable sets is because, it is a handy tool to perform safety verification, among many
Now that we know possible concentration levels after time t apriori, we can check if those concentration levels are indeed withing the safe limits or not. That is, not too high, or not too low.

## Slide 5: Uncertainties with an Example: Anesthesia
A safety critical event that occurs before (almost) all surgeries.
Determining its safety:
Understanding of how it is metabolized.
Its effect on the depth of hypnosis.
UNC Chapel Hill
Safety Analysis Using Reachable Sets
Notes: Now, let’s recall the anesthesia model again.
And we would want to perform safety verification of the model using reachable sets.

## Slide 6: Uncertainties with an Example: Anesthesia
Perform analysis on this model
Safe
Unsafe
Provide certificate
This technique assumes the model is accurate!
I.e., all the parameter values are accurate
Dynamics
Parameters:
Dictated
Notes: Now that we have the dynamics, which is dictated by some parameters \theta_i.
We perform safety analysis on this model, and provide a safety certificate. Which is, safe or unsafe.
However, this techniques assumes that the model is accurate.
That is, the chosen values of the thetas are accurate.

## Slide 7: Uncertainties with an Example: Anesthesia
Analysis
Safe
(Say)
UNC Chapel Hill
Dynamics
Parameters:
Dictated
Notes: Now with this assumption, let’s say we perform our analysis and see that the system is safe.

## Slide 8: Uncertainties with an Example: Anesthesia
Analysis
Safe
(Say)
UNC Chapel Hill
Dynamics
Parameters:
Dictated
Modeling Error!
?
Would it still be safe?
Why modeling error?
Notes: Now, what if we discover a modeling error.
  I.e., the values that we chose for \thetas are not accurate.
  Would it still be safe? We don’t know!
Now the question is, why would there be a modeling error?

## Slide 9: Uncertainties with an Example: Anesthesia
UNC Chapel Hill
Dynamics
Parameters:
Dictated
Modeling Error!
Why modeling error?
Determined empirically – come with errors
Dependent on weight, alveolar volumes etc. –patient specific
Notes: Recall that these parameters we determined empirically. Therefore, they come with errors associated with them.
  Also, these parameters are dependent on patient specific factors such as weight, lung capacity etc..
  So choosing the same fixed set of values, of the parameters, for all patients might not be an accurate way of modeling.

## Slide 10
Verification of Autonomous Systems
Monitoring systems for safety
Safe-workload balancing
Designing of Autonomous Systems
Safe and performance optimal autonomous system
Notes: Two aspects of this course, using 3 examples.

## Slide 11
Verification of Autonomous Systems
Monitoring systems for safety
Safe-workload balancing
Designing of Autonomous Systems
Safe and performance optimal autonomous system

## Slide 12: In the Event of a Crash!
Cause of the crash?
Who was at fault?

## Slide 13: Investigating the Crash
Stores information of the vehicle/plane until the time of crash.
Flight Black Box
Detecting safety violation from the stored information.

## Slide 14: Investigating the Crash: Logging is Expensive!
Flight Black Box
Logging accurately at all time steps is hard!
Sensors are uncertain, on budget systems
Logs sent over unreliable networks
Energy consumption – a concern on intermittently powered devices

## Slide 15: Monitoring: Proposed Strategy
Scattered & Noisy Logs
Bounding Model: Dynamics with Uncertainties
Reconstruct missing logs using reachable sets
Safe or Unsafe?

## Slide 16
Verification of Autonomous Systems
Monitoring systems for safety
Safe-workload balancing
Designing of Autonomous Systems
Safe and performance optimal autonomous system

## Slide 17: Robot Maneuvers
Robot trying to reach its destination, avoiding obstacles.
Obstacles
Nominal Trajectory: Planned Path
Notes: Consider this notion of quantitative safety.

## Slide 18: Robot Maneuvers
But: The robot is running multiple jobs on its processor!
Heat Control
Perception
Path Follower
Multiple Jobs
All jobs cannot always be scheduled—deadline misses!
Responsible for moving the robot along the planned trajectory.
What if the path follower misses its deadline?

## Slide 19: Robot Maneuvers
What if the path follower misses some deadlines?
The trajectory can deviate from the nominal trajectory!

## Slide 20: Robot Maneuvers
What if the path follower misses some deadlines?
The trajectory can deviate from the nominal trajectory!
Trajectory under deadline misses

## Slide 21: Robot Maneuvers
What if the path follower misses deadlines very frequently?
The trajectory can deviate more from the nominal trajectory!

## Slide 22: Robot Maneuvers
What if the path follower misses deadlines very frequently?
The trajectory can deviate more from the nominal trajectory!
And becomes unsafe!

## Slide 23: Robot Maneuvers
In Conclusion: Not all patterns of deadline misses are safe!
Goal: Detect if a given pattern of deadline misses is safe!

## Slide 24
Verification of Autonomous Systems
Monitoring systems for safety
Safe-workload balancing
Designing of Autonomous Systems
Safe and performance optimal autonomous system

## Slide 25: Introduction: Model Selection Problem
A robot needs to perform a task based on its perception, such as autonomous driving
Local: Fast, and less accurate
Cloud: Slow, but highly accurate
Invoke the cloud or not?
Always available
Model Selection Problem

## Slide 26: Optimality: Problem Statement Illustration
Loss
Cost
Local, Local, . . ., Local, Cloud
Local, Cloud, . . ., Cloud, Local
Cloud, Cloud, . . ., Cloud, Cloud
Compute a sequence – without exploring all sequences – that belongs to this region
All Cloud: Cloud, Cloud, . . ., Cloud
All Local: Local, Local, . . ., Local
. . .
. . .
Notes: Here, I propose a strategy, among all possible sequences of invoking the cloud/local model, that has low cost and low loss.
These are the possible sequences of invoking the cloud/local model.

## Slide 27
Trustworthy Autonomy
Formal Methods
Control Theory
Real-Time & Embedded Sys.
Mars rover safe navigation
Crash Detection/Prevention
Logged behavior
Recreated behavior to detect crash
Unsafety
Workload balancing
Heat Control
Perception
Lane Departure
Low bandwidth processor installed on a vehicle
Smartly processes the jobs s.t. the vehicle is safe
Safe, performance optimal maneuvers